Non-Intrusive multi-turn actuators for open-close duty with integral controls AUMATIC

Type SA 07.2 – SA 16.2 with AC 01.2

Version according to wiring diagram TPC A-0A1-1C1-A000 TPA 00R100-3I1-000

- Type of duty: short-time duty S2-15 min

- Output speeds of 4 to 180 rpm at 50 Hz supply

- 3-ph AC motor in insulation class F, with motor protection by three thermoswitches placed in the windings

- Motor without terminal box, internal connection via plug/socket connector

- Anti-condensation heater in switch compartment, internal supply

- Electronic absolute encoder for position and torque sensing

- Handwheel does not rotate during motor operation, with output contact for manual operation

- Valve attachment according to EN ISO 5210

- Connection between actuator and controls via plug/socket connector

- Reversing contactors mechanically and electrically interlocked

- Local controls with operation mode switch, 4 push buttons, 6 indication lights, Bluetooth interface and plaintext display for programming, status, position and fault indication

- Four inputs OPEN - STOP - CLOSE - EMERGENCY 24 V DC galvanically isolated via opto-isolator

- Six freely programmable contacts for output signals on status and faults

- Programmable timer function

- Programmable emergency behaviour

- Programmable torque by-pass

- Galvanically isolated electronic position feedback signal 0/4...20 mA

- Galvanically isolated electronic torque feedback signal 0/4...20 mA

- Electronic device ID, event report, operating data logging and status signals according to NAMUR recommendation NE 107 via display

- Controls or local controls can be positioned at every 90°

- Permissible ambient temperature –25 °C to +70 °C, enclosure protection IP 68, corrosion protection KS

- Finish coating: 2-layer powder coating, colour: silver-grey (similar to RAL 7037)

Options:

- Corrosion protection KX, for installation in atmosphere with a high pollutant concentration

- Continuous mechanical position indication

- Wall bracket for mounting controls separate from actuator

Further options on request