Actuators for modulating duty

Part-turn actuators SQR 05.2 – SQR 14.2

Version according to wiring diagram TPA 00R1AA-0E1-000

- Intermittent duty S4-25% up to 1,500 operations/hour

- Mechanical end stops

- Operating times for 90° at 50 Hz mains frequency from 8 to 100 seconds, depending on the size

- Adjustable swing angle between 75° and 105°

- Self-locking drive system

- 3-phase AC motor in insulation class F with full motor protection by means of 3 thermoswitches integrated in the stator winding

- Motor without terminal box, internal connection via plug/socket connector

- Counter gear mechanism for end positions CLOSED and OPEN without auxiliary voltage

- Tripping torque without auxiliary voltage for directions CLOSE and OPEN, adjustable via calibrated torque dial; value in daNm directly indicated

- Continuous mechanical position indication

- Electronic position transmitter 0/4 – 20mA

- Anti-condensation heater in switch compartment

- Handwheel for manual operation, does not rotate during motor operation

- Valve attachment according to EN ISO 5210/5211

- Connection between actuator and external controls via plug/socket connector

- Permissible ambient temperature –30 °C to +70 °C, enclosure protection IP68, KS corrosion protection

- Top coat: 2-layer powder coating, colour: silver-grey (similar to RAL 7037)

Options:

- KX corrosion protection, for installation in extremely aggressive atmosphere

- Galvanically isolated tandem switches (two NC and NO contacts each)

- Intermediate position switches (DUO switches), separate for OPEN and CLOSE

- Also available as lever actuator with base and lever

- AM or AC controls (refer to separate specification texts)

Other options on request